## Slide 1: Sharing of Interstate transmission charges and losses Regulations
1
By
Shilpa Agarwal
Dy. Chief (Engg.)
CERC

## Slide 2
2
GROWTH OF INDIAN POWER SYSTEM
36874
19858
42131
20000
10000
0
50000
40000
30000
60000
Central Sector
13796
State Sector
15043
Private Sector
XI Plan
XII Plan
26783
Central Sector
State Sector
Private Sector
Total
36874 MW (47%)
15220 MW (28%)
26181 MW (30%)
26783 MW (34%)
16732 MW (30 %)
15530 MW (18 %)
15043 MW (19%)
23011 MW (42 %)
46825 MW (52%)
78700 MW (Rev. 62374)
54963 MW (Achieved)
88536 MW*
XI
XII
*As per draft 12th 5 year plan
Excluding Renewable~30,000 MW

## Slide 3: Sector Overview
3
3
Generation
  Delicensed by EA 2003
  Sold largely under Long term contracts(91%)
  Bilateral contracts for sale of power
Transmission – Used for conveyance of electricity from generation to load centre
  Licensed business
  2 grids- NEW Grid, Southern Grid
  Backbone for interregional transfer at National level
  Ownership-owned largely by Powergrid, Private players are coming up
  Pooled asset, Power flows as per laws of physics and not contracts
Distribution
Segregated Statewise
  Largely with State owned DISTCOs
  Pvt. DISCOMS in metros- Delhi- BSES & NDPL; Mumbai: TATA Power & BSES; CESC in Kolkata, TORRENT in Ahmedabad & Surat; WESCO, SOUTHCO & NESCO in Orissa
  Franchisees in some states; Mah, UP

## Slide 4: Transmission Planning
4

## Slide 5: Background
5
Development of transmission system in the country was traditionally the responsibility of the erstwhile State Electricity Boards (SEBs).
The country’s transmission networks were organised into five regional grids – North, West, South, East and NE.
Grid developed as the Associated Transmission Systems (ATS) for various generation projects. Initially, CGS like NTPC, NHPC etc. too took up the construction of ATS.
Power Grid Corporation of India (PGCIL) was created (originally NPTC) in 1988 with the objective of creating strong regional grids and subsequently a national grid.
PGCIL was entrusted with the task of building inter-state and inter-regional transmission systems.
Various Central GENCO transmission assets were transferred to PGCIL.
Role of transmission system planning for harmonious development was carried out by the Power System wing of the Central Electricity Authority (CEA).

## Slide 6: Planning Framework (Post Electricity Act 2003)
6
Differences on cost sharing have at times delayed/ held up trans. development
National Electricity Policy (NEP) provides “the CEA shall prepare short term and perspective plan”
  Perspective Plan- 15yrs., 3 plan periods
  Short Term- 5yrs., 1 plan period
Transmission mandated as a licensed business.
  2 statutory entities created & assigned roles of transmission system planning & development
    Central Transmission Utility (CTU) & State Transmission Utility (STU).
      CTU responsiblke for inter-state systems
      STU responsible for intra-state systems
    To start with, PGCIL has been designated as the CTU
    The transmission wing of the erstwhile SEBs designated the STUs.
  CTU and STU also deemed licensees- build own, operate and maintain transmission systems
CTU to issue Network Plans and update plans periodically (not later than annually)
  To contain details like identified new lines and substations, system strengthening projects, broad design specs, probable line lengths and substation locations etc.
New transmission planned based on
  Requests by new generators/ application for transmission access
  Identified pockets of congestions based on feedback by RLDC/ SLDC
  Demands by States to meet their load growth
CTU identifies required Transmission based on Load Flow Studies
System discussed and agreed in Regional Standing Committee Meetings
  Chaired by Member (PS), CEA
Cost sharing for new transmission agreed in RPC- consent for signing BPTA

## Slide 7: Planning
7
Generation delicensed with EA2003, private generators were encouraged
Evacuation ensured under Open Access Regulations 2004
Connectivity, Long term Access, Medium term Open Access Regulations 2009, effective from 1.1.2010
2008-Power Exchange operationalised & STOA Regulations notified

## Slide 8
NEWS Grid
NEW Grid
S Grid
Birpara-Salakati 220 kV D/C Line
400 kV Rourkela-Raipur D/C
400 kV Muzaffarpur-Gorakhpur D/C Line
765 kV Raichur-Solapur

## Slide 9
9
Energy Resource Map
Hydro potential in NER and upper part of NR
Coal reserves mainly in ER/ WR
For optimal utilisation of resources – strong National Grid

## Slide 10: Transmission Pricing
10

## Slide 11
11
1000MW
500MW
300MW
200MW
Transmission Charges
(Tariff)
Share
Generation
Tr. Charges
Rs. 50 cr
Rs.25cr
Rs.15cr
Rs.10cr
Sharing of Tr, Charges based on Contracts
Beneficiaries of Generation are SYNONYMOUS with Users of Tr. System
Since Beneficiaries are identifiable their consent is obtainable
Mechanism for Investment consent

## Slide 12
12
1000MW
500MW
300MW
200MW
Benefits of Tr. Systems are shared by all the stakeholders
Mechanism for Investment consent… in reality

## Slide 13
13
Old mechanism for sharing Tr. charges
Rs.
+
Rs.
Cost
Plus
Allocation
Based on entitlements (MW) of
inter-state generating stations
Rs.
Tr. Charges
Rs.
Rs.
Rs.
Rs.
Predominantly Regional
Eg. Southern Region
AP KN TN Kerala

## Slide 14: Pricing under Postage Stamp (Long term User) – An Example
14
Exporting Region- NER
Loss 4%
Importing Region - NR
Pooling stn.
TC=20
Loss 4%
400 km ~ 20 ps/kwh. Loss 2%
Rs. 3 per kwh
Intermediate Region - ER
TC=20
Loss 4%
De - Pooling stn.
TC=20
100 km ~ 10 ps/kwh. Loss 2%
Cost of delivery
  Cost at Generator Terminals – 300 ps/kwh
  Transmission costs to load centre – 90 ps/kwh
  Cost of losses – 74.28 ps/kwh
  Final costs – 464.28 ps/kwh
Much of the cost levels are genuine. There could even be element of cross-subsidisation of new transmission costs by existing beneficiaries
If new line costs are loaded on to first user(s), then the cost of delivery can be prohibitive
There could be a tendency of over-estimation of losses
Hence the need to ensure a fairer allocation

## Slide 15: Evolution of Transmission Pricing
15
Reference:राष्ट्रीय भार प्रेषण केंद्र

## Slide 16
16
National Electricity Policy mandates development of a strong National Grid.
  require transmission prices to be distance and direction sensitive, independent of BPTA and reflect the utilization of the network by each network user
Tariff Policy further requires that such pricing mechanism be implemented by Apr-06.
… the need for revisiting the Transmission pricing
Individual Transmission Licensee raise the bill and maintain payment Security
Mechanism.
Evolution of open access and competitive power markets
  Bilateral transactions, Px
Pricing inefficiency in the emerging circumstances – the problem of pancaking
Changing nature of use of the transmission system by various users- Merchant generators

## Slide 17
17
1000MW
500MW
300MW
200MW
Sharing of Tr, Charges is based on flow of power / utilization
Beneficiaries of Generation are NOT SYNONYMOUS with Users of Tr. System
In fact they are Anonymous
Users are beyond boundaries
Beneficiaries are not identifiable. Consent from Whom ?
Discussion with All. Thereafter obtain Regulatory approval

## Slide 18: Regulatory facilitations
18
Grant of Regulatory Approval for execution of Inter-State Transmission Scheme to Central Transmission Utility Regulations, 2010
  For projects where PPA for entire capacity has not been signed and applied Long term Access under Regulations 2009
  System Strengthening lines
  CTU could proceed without BPTA based on such approval
  Examples: System asociated with Krisnapatnam

## Slide 19: Sharing of Interstate Transmission Charges & Losses Regulations 2010
19
Regulation dated 15.06.2010
Effective from 1.7.2011
Remain in force till 1.7.2016
Transmission charges for the Assets of ISTS licensees / non-ISTS licensees shall continue to be determined by respective Commission.
No change in Annual Tariff recoverable for ISTS licensee…. Revenue neutral
Sharing based on Point of Connection (PoC) Tariffs based on load flow analysis to capture distance and direction vectors also
Load flow analysis to be carried out by NLDC who is designated as the Implementing Agency for the initial two years.
PoC Charges to be paid by generators & discoms
  For Long term customers of ISGS, charges payable by such generators shall be billed directly to customers post COD of generator

## Slide 20
20
20
ISTS
Deemed ISTS (Owned by States)
ISTS (POWERGRID, IPTCs)
The Pooled charges are recovered from Demand Customers as well as Generators
CTU vested with the responsibility of Billing, Collecting and Disbursement (BCD) of the Transmission Charges on behalf of all the ISTS licensees. Revenue Sharing Agreement (RSA) prepared by CTU
Transmission charges are determined by CERC (Section 61,62 or 63 of EA 2003)
Charges of all ISTS (POWERGRID, Reliance etc.) to be pooled together
Charges of Non-ISTS systems (certain State transmission systems) as approved by RPC/CERC shall also be considered in the pool… Deemed ISTS
Transmission Charges
(POWERGRID, IPTCs, Deemed ISTS)
Demand Customers
Generators
Designated ISTS Customers
Designated ISTS Customers
As per the new Regulation

## Slide 21: Principles of sharing ISTS charges and losses
21

## Slide 22: Principles of sharing ISTS charges and losses
22
Factors to be calculated
  Point of connection charges – in terms of
    RS./MW/month for LT/MT access
    paise/kwh for STOA
  Loss allocations factors
  Load flow based methods to be used for calculating above factors
PoC charges Methodology-Hybrid method & Uniform Charge Sharing Mechanism
  Hybrid Methodology: Cost Allocation through marginal usage; Slack bus identification through Average Participation Method.
  Uniform Charge Sharing Method: Present Methodology of Regional Postage Stamp Method
  For 1st 2 years- 50% charges will be recovered through Hybrid method & 50% through Uniform charge sharing method.
  After 2 years weightage to be reviewed
Data to be provided by DIC to IA by end of Nov, each year. Else Commission may authorize IA to obtain such information from alternative sources.- as per Procedure issued by NLDC
The Yearly Transmission Charge of the ISTS Licensees shall be fully and exactly recovered. There shall be periodic truing up of YTC as per actual billing.
Solar Based Generation
  No. Tr. Charges/Tr. Losses for use of ISTS for the useful life of the projects commissioned in next 3 yrs. (July 2014)

## Slide 23
23
Hybrid Method
Marginal Participation + Average Participation
Methods employed in arriving at Point of Connection Charges
Uniform Charging Method
Plus

## Slide 24
24
24
200MW
800MW
600MW
400MW
600MW
400MW
600 x 800 = 480MW
1000
600 x 200 = 120MW
1000
400 x 800 = 320MW
1000
400 x 200 = 80MW
1000
Average Participation
A
200MW
B
800MW
Area of influence

## Slide 25
25
G2
500MW
G1
600MW
D3
400MW
D2
100MW
D1
600MW
250
400
150
50
200
250
*Indicative only
Power flow in lines in MW
Marginal Participation
A
B
+ 1MW
(4/11)
(1/11)
(6/11)

## Slide 26
26
G2
500MW
G1
600MW
D3
400MW
D2
100MW
D1
600MW
250
400
150
50
200
250
*Indicative only
Power flow in lines in MW
Marginal Participation
A
B
+ 1MW
(5/11)
(6/11)

## Slide 27
27
 | Transmission charges |  | Rs.100 | cr |  | 
Users | Base Flow | Flow due to Increments | Changes | Only + changes | Participation factor | Share of Tr. Charges
G1 | 200 | 200.5 | 0.5 | 0.5 | 0.3125 | 31.25
G2 | 200 | 200.8 | 0.8 | 0.8 | 0.5 | 50
D1 | 200 | 198 | -2 | 0 | 0 | 0
D2 | 200 | 200.2 | 0.2 | 0.2 | 0.125 | 12.5
D3 | 200 | 200.1 | 0.1 | 0.1 | 0.0625 | 6.25
 |  |  |  | 1.6 | 1 | 100
Line AB
BC + CD +EF+…
Point Tariff
Marginal Participation
G2
500MW
G1
600MW
D3
400MW
D2
100MW
D1
600MW
250
400
150
50
200
250
A
B
* Identification of the slack node(s) changes the rule of the game

## Slide 28
28
Uniform Charging Method
Total YTC in Rupees
Approved injection in MW
Approved withdrawal in MW
+
=
‘U’ Rs./ MW
‘U’ Rs./MW is charged for each MW (Approved Injection & Withdrawal)
U x (Approved injection in MW + Approved withdrawal in MW) = Total YTC

## Slide 29
29
Reimbursed
Next Month
To 1st bill
payers
X 1
X 1.25
Over Inj./Drawal
>20% Appr.(Metered)
Over Inj/Drawal
<=20% Appr. (Metered)
DIC triggered (Monthly)
BIN-4
DIC Specific
X 1
Addl. Appr. MT
System triggered (Monthly)
BIN-2
DIC Specific
50% YTC
50% YTC
Inputs forecast
for each scenario
Process
(Software)
O/P(Ex-ante)
for each month
TRO
DIC
BIN-1
100% YTC
Based on
PoC for
each DIC
YTC=∑PoC1 x MW1
Drawal MW
(Approved LT.MT)
Injection MW
(Approved LT.MT)
YTC(>=400kV)
Network
O/P
Process
Flow chart for Sharing of Charges
Hybrid
(~100% YTC)
UC
(=100%YTC)
TRO : Transmission Owners
DIC : Designated ISTS Customers
YTC : Yearly Transmission Charges
PoC : Point of Connection Charge
UC : Uniform Charge
A d j u s t m e n t (POST-FACTO)
B a s i c Transmission Charges (EX-ANTE)
FERV, Interest
rates, etc.,
BIN-3
In
proportion
to Appr.
Inj & Drawal
for each DIC
Change in YTC due
to revised commng.
of TRO Network
TRO triggered (Bi-Annual)
Sharing of Inter state Transmission charges and losses

## Slide 30: Billing- Four Parts
30
First Part
Raised on 1st working day of each month for previous month, determined prior to application period
Charges for use of transmission assets based on PoC method.
[PoC Tr. Charge of generation zone in Rs/MW/month for peak hrs.]X[(Approved injection for peak hours)]+
[PoC Tr. Charge of generation zone in Rs/MW/month for other than peak hrs.]X[(Approved injection for other than peak hours)]
Similar to first part to recover additional MTOA charges
Second Part
Raised along with first part of the bill
Third Part
Raised on first working day of September and March for the previous six months.
To adjust any variations in interest rates, FERV,rescheduling of commissioning of transmission assets, etc. as allowed by the Commission for any ISTS Transmission Licensee.
Total amount to be recovered /reimbursed because of such under recovery / over recovery shall be billed by CTU to each DIC in proportion of its average Approved Injection /Approved Withdrawal over previous six months on a biannual basis.
Fourth Part
Raised within 3 working days of issuance of Regional Tr. Deviation A/c by RPCs.
Additional bill for deviations- shall be charged seperately
First 20% deviation-zonal PoC charges
Beyond 20% deviation- 1.25 times zonal PoC charges
A generator instead of injecting, withdraws from the grid- Case of Commissioning power -1.25 times zonal PoC charges
To be raised/collected by CTU
Redistribute to Tr. licensees in proportion to their Monthly Tr. charges

## Slide 31
31
31
Based on PoC
Hybrid method
(Marginal & Average participation methods)
+
Uniform method
PoC: Indicative only in Rs.Lakh/MW/Annum
Initially NEW and SR separately
1000MW
2000MW
800MW
600MW
500MW
900MW
Rs. .8
Rs.1
Rs. 1.1
Rs. .85
Rs.0.9
Rs. 0.9
For
A
Set
Period
ISTS charges
(POWERGRID, IPTCs, Deemed ISTS etc.)
National Game
Generation Access zones
Demand Access zones
Based on forecast commitments of
Total Yearly Transmission Charges (YTC)
Demand & Generation in MW
Total network
As per the new Regulation

## Slide 32: Commercial Agreements
32

## Slide 33
33
a) Transmission Service Agreement (TSA)
Sharing of Inter state Transmission charges and losses
Between CTU, USERS (DICs) and ISTS licensees
Interalia covers the USERS to pay the PoC charge which covers the revenue of ISTS licensees
All USERS shall be default signatories to the TSA
The commercial arrangement would facilitate financial closure of transmission investment
Effective Post COD of the line. Before COD of line it shall be governed as per existing mechanism of Indemnification, BPTA etc
NTPC also to become signatory to TSA as generator.
Model TSA notified by CERC dated 29.04.2011. Model TSA is a deemed signed document as per CERC Order dated 25.01.2012. CERC directed vide Order dated 1.05.2013 directed all DICs to sign TSA within 1month.
Payment security mechanism
Default and its consequences; Dispute resolution mechanisms
Term of the Agreement and termination provisions; Force majeure conditions
b) Revenue Sharing Agreement (RSA)
To be signed among CTU & other transmission Service providers.
  Detailed commercial and administrative provisions related to disbursement of ISTS charges

## Slide 34: Sample PoC Charges notified from July 2014- September 2014
34

## Slide 35: Third Amendment effective from 1.5.2015

## Slide 36: Scope
Definition of approved injection and withdrawal based on peak.
Removal of Uniform charges
Slabs- 3 to 9
Computation based on peak scenario.
No truncation of network.
STOA adjustment.
ISTS charges and losses for Solar Power
Transmission charges of State Lines based on % usage
Sharing of injection charges for Tied up power
State embedded generators to pay for ISTS usage.
HVDC Charges sharing
Reliability Charge

## Slide 37
“(c) ‘Approved Injection’ means the injection in MW computed by the Implementing Agency for each Application Period on the basis of maximum injection made during the corresponding Application Periods of last three (3) years and validated by the Validation Committee for the DICs at the ex-bus of the generators or any other injection point of the DICs into the ISTS, and taking into account the generation data submitted by the DICs incorporating total injection into the grid:
Provided that the overload capability of a generating unit shall not be used for calculating the approved injection:
Provided further that where long term access (LTA) has been granted by the CTU, the LTA quantum, and where long term access has not been granted by the CTU, the installed capacity of the generating unit excluding the auxiliary power consumption, shall be considered for the purpose of computation of approved injection."

## Slide 38
“(f) ‘Approved Withdrawal’ means the withdrawal in MW computed by the Implementing Agency for each application period on the basis of the actual peak met during the corresponding application periods of last three (3) years and validated by the Validation Committee for any DIC in a control area after taking into account the aggregated withdrawal from all nodes to which DIC is connected and which affect the flow in the ISTS, and the anticipated maximum demand to be met as submitted by the DIC:
Provided that the overload capability of a generating unit in which the DIC has an allocation or with which the DIC has signed an agreement, shall not be used for calculating the approved withdrawal under long term access (LTA).”

## Slide 39: Methodology for Calculation of forecasted maximum generation/withdrawal of DICs for vetting by Implementing Agency
For Demand data:
The projected maximum withdrawal figures provided by DICs will be vetted by Implementing Agency based on the following:
Monthly peak demand met for each State/UT in the last 3 years for the period corresponding to the Application Period shall be considered.
The average of monthly peak demand met for each State/UT in each of the last 3 years for the period corresponding to the Application Period shall be calculated.
The average peak demand met for each State/UT for the Application Period shall be projected based on last 3 year’s average of monthly peak demand met figures.
Similarly All India peak demand met in last 3 years shall be averaged for the period corresponding to the Application Period. This shall be projected for the ensuing Application Period. The projected peak demand of each State/UT thus arrived shall be normalized with the projected All-India peak demand met of the Application Period under consideration for the current year.
For Generation Data:
….Similarly maximum injection data (for last 3 years as well as projected for the ensuing quarter) for generators embedded within the State system shall be provided by respective SLDC. In case data is not provided by SLDC to the Implementing Agency, the maximum injection of the concerned State shall be taken as the difference between peak met and withdrawal from ISTS based on actual metered data (for the time block corresponding to the block in which peak met occurred).
b. If sum of projected generation in the grid is more than sum of projected demand, the generation may be proportionately reduced to match sum of withdrawal data. If sum of projected generation in the grid is less than sum of projected demand, the demand may be proportionately reduced to match sum of generation.

## Slide 40: Slabs
9 slabs for transmission charges
9 slabs for transmission losses.
  There shall be 4 steps above the average loss and 4 steps below the average loss with a slab size of 0.25% subject to minimum loss of Zero percent.
The slabs may be reviewed by the Commission after two years.

## Slide 41: Methodology for calculation of slab rates
The POC rates shall be arrived at by dividing the quantum of charges allocated to each zone by its LTA+MTOA.
The PoC rates so arrived shall be adjusted based on average rate and one sigma deviation on either side. The difference between maximum rate and minimum rate so arrived shall be divided by eight to determine width of each slab. The POC rates for all entities shall be placed in appropriate slab, minimizing the distance from slab rate as per its adjusted rate calculated after accounting for standard deviation. The rates may be scaled up/down as required.
For the purpose of STOA, collective transactions and computation of transmission deviation charges, there shall be separate slabs for injection and withdrawal rates.

## Slide 42: HVDC Charge payment
10% of Monthly Transmission Charges (MTC) of HVDC transmission system shall form part of Reliability Support Charges and the balance shall be billed as detailed below:
Transmission charges for HVDC system created to supply power to specific regions shall be borne by DICs of such regions. The HVDC Charge shall be payable by DICs of the Region in proportion to their Approved Withdrawal. In case of Injection DICs having Long Term Access to target region, it shall also be payable in proportion to their Approved Injection.
Where transmission charges for any HVDC system are to be partly borne by a DIC (injecting DIC or withdrawal DIC, as the case may be) under a PPA or any other arrangement, transmission charges in proportion to the share of capacity in accordance with the PPA or other arrangement shall be borne by such DIC and the charges for balance capacity shall be borne by the remaining DICs by scaling up of MTC of the AC system included in the PoC. Such HVDC shall not be considered under (i) above.
B/B by scaling up YTC.

## Slide 43: Reliability Charge Calculation
Reliability Support Charge means the Charge for reliability benefits which accrue to the DICs by virtue of operating in an integrated grid.
10 % of MTC including HVDC B/B +10% HVDC for specific region.

## Slide 44: Payment in case of delay of generator
“Where the Approved Withdrawal or Approved Injection in case of a DIC is not materializing either partly or fully for any reason whatsoever, the concerned DIC shall be obliged to pay the transmission charges allocated under these regulations:
Provided that in case the commissioning of a generating station or unit thereof is delayed, the generator shall be liable to pay Withdrawal Charges corresponding to its Long term Access from the date the Long Term Access granted by CTU becomes effective. The Withdrawal Charges shall be at the average withdrawal rate of the target region:
Provided further that where the operationalization of LTA is contingent upon commissioning of several transmission lines or elements and only some of the transmission lines or elements have been declared commercial, the generator shall pay the transmission charges for LTA operationalised corresponding to the transmission system commissioned:
Provided also that where the construction of dedicated transmission line has been taken up by the CTU or the transmission licensee, the transmission charges for such dedicated transmission line shall be payable by the generator as provided in the Regulation 8 (8) of the Connectivity Regulations:
Provided also that during the period when a generating station draws start-up power or injects infirm power before commencement of LTA, withdrawal or injection charges corresponding to the actual injection or withdrawal shall be payable by the generating station and such amount shall be adjusted in the next quarter, from the ISTS transmission charges to be recovered through PoC mechanism from all DICs:

## Slide 45: DIC
(l) Designated ISTS Customer or DIC means the user of any segment(s) or element(s) of the ISTS and shall include generator, State Transmission Utility, State Electricity Board or load serving entity including Bulk Consumer and any other entity or person directly connected to the ISTS and shall further include any intra-State entity who has obtained Medium Term Open Access or Long Term Access to ISTS.

## Slide 46: Thank You

## Slide 47: Maharashtra

## Slide 48: Maharashtra drawal-MW